# GENERAL DESCRIPTION

# W26 transceiver unit is designed for reading code from uem4100 compatible read-only tags and is a major component in RFID(Radio Frequency Identification) reader system. It can be applied in office/home security, personal identification, access control, anti-forgery, interactive toy and production control systems etc.

# FEATURES

- Built-in transceiver antenna;

- Maximum effective distance up to 180mm;

- Less than 100ms decoding time;

- Low power dissipation with single power supply;

- Wiegand 26bits and ABA TRACK2 Format interface optional;

- Support uem4100 compatible read only tags(64Bits,Manchester coding);

- Built-in bi-color LED and buzzer.

# INTERFACE DESCRIPTION

| NUMBER | COLOR | SYMBOL | DESCRIPTION |
| --- | --- | --- | --- |
| 1 | Red | VCC | Positive Power Supply |
| 2 | Black | GND | GND |
| 3 | Green | WD0 (DATA) | Output as DATA0 in Wiegand and DATA in ABA |
| 4 | White | WD1 (CLK) | Output as DATA1 in Wiegand and CLK in ABA |
| 5 | Brown | HOLD (CP) | Output as HOLD in Wiegand and CARD PRESENT in ABA |
| 6 | Yellow | SEL | Wiegand/ABA selection NC : Wiegand GND: ABA |
| 7 | Blue | LED | Input, internally pulled up to +5V. Connected to GND will change the color of LED. |
| 8 | Grey | BUZ | Input, internally pulled up to +5V. Connected to GND will activate the BUZZER. |

CHARACTERISTICS

- Absolute Maximum Ratings

| ITEM | SYMBOL | VALUE | UNIT |
| --- | --- | --- | --- |
| Power Supply | VCC | 15 | V |
| Operating Temp. | TOPR | 0~+70 | ℃ |
| Storage Temp. | TSTR | -55~+125 | ℃ |

- Electrical and Mechanical Specification

Under TA＝25℃，VCC＝+12V unless specified

| ITEM | SYMBOL | MIN | TYP | MAX | UNIT |
| --- | --- | --- | --- | --- | --- |
| Power Supply | VCC | 10 |  | 15 | V |
| Current Supply | IC |  | 65 | 80 | mA |
| Operation Freq. | FREQ | 100 | 125 | 150 | KHZ |
| Effective Distance* | DIS | 0 | 100 | 150 | mm |
| Decoding Time | TDEC |  | 65 | 100 | ms |

- Effective Distance depends on tags and operating environment.

APPLICATION INFORMATION

- TAG DATA FORMAT

W26 support uem4100 compatible 64bits read only tags with Manchester Coding and RF/64 data rate.

| 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| ROW0 ROW1 ROW2 ROW3 ROW4 ROW5 ROW6 ROW7 ROW8 ROW9 | D00 | D01 | D02 | D03 | PR0 |
|  | D10 | D11 | D12 | D13 | PR1 |
|  | D20 | D21 | D22 | D23 | PR2 |
|  | D30 | D31 | D32 | D33 | PR3 |
|  | D40 | D41 | D42 | D43 | PR4 |
|  | D50 | D51 | D52 | D53 | PR5 |
|  | D60 | D61 | D62 | D63 | PR6 |
|  | D70 | D71 | D72 | D73 | PR7 |
|  | D80 | D81 | D82 | D83 | PR8 |
|  | D90 | D91 | D92 | D93 | PR9 |
|  | PC0 | PC1 | PC2 | PC3 | 0 |

- The header format is 9 digits of  ‘1’;

- D00~D93 are data bits for user;

- PR0~PR9 are the row even parity check bits;

- PC0~PC3 are the column parity check bits;

- The last data is fixed to “0”.

- Wiegand 26bits Format Interface

Wiegand 26bits Format Interface comprises of 26bits data including 24 user bits and 2 parity check bits. The 24 user bits correspond to the latter 40 user bits in tags.

| Bit | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | PE | D | D | D | D | D | D | D | D | D | D | D | D | D | D | D | D | D | D | D | D | D | D | D | D | PO |
|  |  | E | E | E | E | E | E | E | E | E | E | E | E | O | O | O | O | O | O | O | O | O | O | O | O |  |
|  |  | D40 | D41 | D42 | D43 | D50 | D51 | D52 | D53 | D60 | D61 | D62 | D63 | D70 | D71 | D72 | D73 | D80 | D81 | D82 | D83 | D90 | D91 | D92 | D93 |  |

- PE as even parity check bit and PO as odd parity check bit;

- The bits marked with E go for even parity check and the bits marked with O go for odd parity check;

- Wiegand 26bits Format Timing

| SYMBOL | DESCRIPTION | VALUE( Typ. ) |
| --- | --- | --- |
| THD | Sending Start Delay | 0.06ms |
| TSD | Sending Stop Delay | 2ms |
| TDW | Data pulse width | 0.4ms |
| TIW | Data pulse interval width | 2ms |

- ABA TRACK2 Format Interface

Structure of ABA TRACK2 data message is :

0000000000 11010 1248P 1248P 1248P 1248P 1248P 1248P 1248P 1248P 1248P 1248P 11111 LRC 00000

- Leading Zero is 0 of 10 digits;

- Start Char is HEX “B” (11010,Low bit first,1248P, P is Bit Odd Parity);

- Card Number is 0000000000~9999999999(10 digits) with most significant digit first;

- End Char is HEX “F” (11111, Low bit first,1248P, P is Bit Odd Parity);

- Longitudinal Redundancy Check(LRC) is Even Parity check(excluding the parity bit);

- Trailing Zero is 0 of 5 digits;

- Data transferred LSB first.

- Example:

B0  B1  B2  B3  P

Start Char:       1   1    0   1   0

Card Data:        1   0    0   0   0

0   1    0   0   0

1   1    0   0   1

End Char:         1   1    1   1   1

LRC:               0   0    1   0   0

- ABA TRACK2 Format Timing

| SYMBOL | DESCRIPTION | VALUE( Typ. ) |
| --- | --- | --- |
| THD | Start Delay | 0.5ms |
| TSD | Stop Delay | 0.5ms |
| TCL | CLK pulse low width | 0.5ms |
| TCH | CLK pulse high width | 0.5ms |